## Slide 2
Control Plan

## Slide 3
3
Control Plans:
Control the risks identified in the P-FMEA (High RPNs)
A structured approach to control process and product characteristics
Focusses on Customer Requirements
Assure reaction plans are in place in case of out-of-control conditions
Provide a central document for communication of control methods
A Control Plan contains following key information:
  Identification of the control factors
  The specifications and tolerances
  The measurement system
  Sample size and frequency
  The control method
  The reaction plan
Control Plans are living documents, just like FMEA’s
Control Plan

## Slide 4
Objectives of the training:
To understand the use of a Control Plan
To learn the steps to develop a Control Plan
To learn how to link each control plan step to the FMEA
4
Control Plan, Objectives

## Slide 5
Control Plan, a systemic way to Control a process:
  Define Characteristics per process step:
    Machines, Devices, Jigs and Tools
    Product, Process and Special characteristics
  Define Methods per process step:
    Process and Product Specifications and Tolerances
    Measurement and Inspection techniques
    Sample size and frequency
  Actions that should be taken in case of Non-Conformities
5
Control Plan, Summary

## Slide 6
Page 6
Control Plan, a systemic way to Control a process:
Verify if defined steps are followed
Audit the process by Control Plan on a regular base
Update the Control Plan consistently
6
Control Plan, Summary

## Slide 7
7
Control Plan, Inputs
Control Plan, inputs might include following tools:
  FMEA
  Flow Chart (process sequence)
  Lay-out Plan production line
  Sequence Of Events
  Part Number/ Tooling / Tool List
  Assembly Drawing
  Specifications/ Dimensions/ Tolerances
  CTQ List
  Process Map
  Historical OMS

## Slide 8
A build
B build
Pilot
Drawing
Issue part approval form
Tool development
FMEA + control plan
Conditional approval
HVPT approval
Part approval
Quality and capacity confirmation
HVPT process approval
Fit / performance
Purchasing
SQE
QA
Source
SQE approval
Issue HF PA requirements
HF proto part approval
HF full part approval (OT/OP)
MF and LF part receipt
Inspection OK – NOK send CAR’s
VCB approval
SOP
Control Plans, Planning

## Slide 9
A
B
C
D
Part /
Process
Number
Process Name /
Operation Description
Machine Device
Jig. Tools
for Manufacturing
No.
Evaluation
Measurement
Technique
Product
Process
Product/Process
Specification
tolerance
Special
Characteristics
Class
Size
Control
Method
Freq.
Reaction
Plan
Sample
Methods
Characteristics
Prototype
Pre-launch
Production
Control Plan Number
Key Contact/Phone
Date (Original)
Date (Revised)
Part Number/Latest Change Level
Part Number / Description
Plant / Supplier
Supplier Code
Core Team
Plant / Supplier Approval Date
Customer Eng.'s Approval / Date (if Required)
Customer Quality Approval / Date (if Required)
Other Approval / Date (if Required)
1
2
5
6
7
8
9
10
11
12
3
4
Advanced Product Quality Planning (APQP) Reference Manual, QS-9000
Control Plans
Operation
Characteristics
Methods
Reaction
Plan

## Slide 10
1. Part/Process Number:
  Usually referenced from the process flow chart, PFMEA or Tool sheets
2. Process Name/Operation Description:
  Identify the process/operation that best describes the activity being addressed (e.g. work elements)
  Use verb / noun format
3. Machine, Device, Jig, Tools for Manufacturing:
  Identify the processing equipment required. (e.g.. machine, device, jig power tools, assist arms, conveyors, etc.)
  What is being done?
A
Operation
Control Plans

## Slide 11
4. Number:
  Identifies the cross reference number from the applicable documentation.
7. Special Characteristic:
  key processes (e.g. Delta K, QS)
5. Product Characteristic:
  Distinguishing features and/or attributes
6. Process Characteristic:
  Characteristics of the process
  What is Important?
B
Characteristics
Control Plans

## Slide 12
PRODUCT CHARACTERISTIC
  physical properties of the part
  Identified important customer characteristics (CTQs and Delta-K)
Examples: length, width, tensile strength, torque, weld integrity, color, alignment, etc.
A description of the state of the component or vehicle after the particular operation is completed
PROCESS CHARACTERISTIC
  identify characteristics, which when controlled, reduce variation in product characteristics
Examples: pressure, temperature, force, feed rate, RPM (torque), etc.
Related to product characteristics
  Characteristics: Identify Product and Process characteristics for each Control Plan step
Control Plans

## Slide 13
8. Product/Process Specification:
  Specifications/tolerance for a part or process. (eg. may be obtained from various engineering documents)
9. Evaluation/Measurement Technique:
  Identifies the measurement system being used to measure product/process characteristics. (eg. gages, fixtures, test equipment, blocks, go/no go, etc)
10 / 11. Sample Size/Frequency:
  List sample size and frequency to perform evaluation. (eg. size: 4 pieces / frequency: fifth time per shift)
  What is the Means for Controlling?
Methods
Control Plans
C

## Slide 14
    Control Plan, Sample size and frequency
Until a process is Capable (Cpk 1.33), 100% Inspection is required
If process is Capable, define Sample Size and Frequency reflecting acceptable risk
Use Six Sigma tools and techniques to control the Process
Counting Defects
C-Graph of Defects
SPC Chart
Capability Graph

## Slide 15
12. Control Method:
  Brief description of how the operation will be controlled
  When selecting the method of control, focus on:
    process control rather than product control
    prevention rather than detection
    targeting nominal rather than specification limits
  Examples:
    Check sheets (weld, quality, tool, material, etc)
    Preventative tooling maintenance
    Variation control charts
    Error/mistake proofing
    SPC charts
Methods
Control Plans, Control Method
C

## Slide 16
13. Reaction Plan:
  Specifies who to inform to make a decision or what to do when a process goes out of control
  Written for people closest to the process (e.g. replace a drill)
  Review systemic root cause and update the FMEA
  Examples:
    Call supervisor
    100% Inspection until the process is back in control
    Calibrate equipment
D
Reaction Plan
Control Plans, Reaction Plan

## Slide 17
Control Plans, Plug Example

## Slide 18
Control Plans, Next Steps
Next Steps to HYMH Suppliers:
Know your customers’ expectations - CTQ’s (Critical to Quality Characteristics)
Have a defined and documented production process (SOE)
Follow 5S Principles
Employ a formal training system
Involve the people on the shop floor
Audit the production process constantly
Manage supplied parts and control supplier performance
Measure/monitor key quality performance indicators
Use an effective Corrective & Preventative Action Process
FMEA and Control Plans are mandatory for PPAP submission level 3.

## Slide 19
Control Plans, Next Steps

## Slide 20
List of acronyms:
CTQ: Critical To Quality, a characteristic judged to be important to the fit and function of a component or assembly as well as customer satisfaction
FMEA: Failure Mode and Effect Analysis
ICAM: Interactive Corrective Action Management
OMS: Operational Method Sheet
Off Tool: (Production Tooling) - When a part is said to be “Off Tool” it is required that the part be manufactured using the exact tooling which will be used for long-term production. This does NOT mean the parts were manufactured from tooling that is “like” or “similar” to the intended production tooling.
Off Process:(Production Process) – When a part is said to be “Off Process” it is required that the part be manufactured and tested using the exact process that will be used for long-term production. This does NOT mean the parts were manufactured using a “like” or “similar” or less than 100% completed process.
P.A.: Part Approval process to determine if part characteristics and specifications are understood and met by the supplier.
PCR: Process Change Request
PFD: Process Flow Diagram
SQM: Supplier Quality Manual
QFD: Quality Function Deployment
QS-9000, PPAP: Product Part Approval Process
QS-9000, APQP: Advanced Project Quality Plan