## Slide 2
Purpose of the FMEA
Preventive costs to identify potential defects by FMEA’s are relatively low compared to in-house detection and correction of defects and even much lower than recovery costs in case defects are found by our Customers.
Identify and eliminate potential defects
Detection and correction of defects
Detection and correction EXTERNAL defects
Customer
Product development
Project planning
D-FMEA
Pre-
production
Production
Lifetime
Validation tests
Preventive costs
Warranty costs
P-FMEA
Cost of validation
Manufacturer / supplier

## Slide 3
Purpose of the FMEA:
  Methodology that facilitates process improvement
  Identifies and eliminates concerns early in the development of a process or design
  Improve internal and external customer satisfaction
  Risk Management tool, focuses on prevention
  FMEA may be a customer requirement (likely contractual, Level 3 PPAP, ISO 9001)
3
Purpose of the FMEA

## Slide 4
Learning FMEA, Training Objectives
Training Objectives:
To understand the use of Failure Modes and Effect Analysis(FMEA)
To learn the steps to developing FMEAs
To summarize the different types of FMEAs
To learn how to link the FMEA to other Process tools
4

## Slide 5
FMEA, Summary
FMEA, a mathematical way to identify:
  Failure modes, the ways in which a product or process can fail
  The Effects and Severity of a failure mode
  Potential causes of the failure mode
  The Occurrence of a failure mode
  The Detection of a failure mode
  The level of risk (Risk Priority Number)
  Actions that should be taken to reduce the RPN
5
  RPN = Severity X Occurrence X Detection

## Slide 6
6
FMEA, Inputs
Inputs might include other tools such as:
D-FMEA (Part and Assembly level) Defines VOC
  Customer requirements
  CTQ Flow down analysis
  Quality Function Deployment (House Of Quality)
  Risk assessments
P-FMEA (Process level) Delivers VOC
  Process flowchart
  Sequence Of Events
  Process Tooling
  Poka-Yoke list

## Slide 7
FMEA, Application Examples
There are several situations where an FMEA is the optimal tool to identify risk:
Process-FMEA:
  Introducing a new process
  Reviewing existing processes after modifications
  Introduce new Part Numbers on an existing Production Line
Design-FMEA:
  Introducing a new Design, Part, Sub Assembly or Assembly
  Use an existing Design for another application
  Reviewing existing Designs after modifications
7

## Slide 8
What Is A Failure Mode?
A Failure Mode is:
  The way in which the component, subassembly, product or process could fail to perform its intended function
  Failure modes may be the result of previous operations or may cause next operations to fail
  Things that could go wrong INTERNALLY:
    Warehouse
    Production Process
  Things that could go wrong EXTERNALLY:
    Supplier Location
    Final Customer
8

## Slide 9
When to Conduct an FMEA
When to Conduct an FMEA?
Early in the New Product Introduction (A-Build) complete for B build.
When new systems, products, and processes are being designed
When existing designs or processes are being changed, FMEA’s to be updated
When process improvements are made due to Corrective Action Requests
9

## Slide 10
10
History of FMEA
10
History of FMEA:
First used in the 1960’s in the Aerospace Industry during the Apollo Missions
In 1974, the Navy developed MIL-STD-1629 regarding the use of FMEA
In the late 1970’s, the Automotive Industry was driven by liability costs to use the FMEA
Later, the Automotive Industry saw the advantages of using this tool to reduce risks related to poor Quality (QS-9000, VDA and ISO-TS 16949 Standards)

## Slide 11
Types of FMEAs
Design FMEA
  Analyzes product design before release to production, with a focus on product function
  Analyzes systems and subsystems in early concept and design stages
Process FMEA
  Used to analyze manufacturing and assembly processes before they are implemented
11

## Slide 12
FMEA: A Team Tool
A team approach is necessary
Team should be led by the Right person, Design, Manufacturing
or Quality Engineer, etc…familiar with FMEA
The following Team members should be considered:
  Design Engineers
  Process Engineers
  Supply Chain Engineers
  Line Design Engineers
  Suppliers
  Operators
  Practical Experts
12

## Slide 13
The FMEA Form
13
Identify failure modes and their effects
Identify causes of the failure modes
and controls
Prioritize
Determine and assess actions

## Slide 14
FMEA Procedure
1. For each process input determine the ways in which the input can go wrong (failure mode)
2. For each failure mode, determine effects
  Select a Severity level for each effect
3. Identify potential causes of each failure mode
  Select an Occurrence level for each cause
4. List current controls for each cause
  Select a Detection level for each cause
14
  RPN = Severity X Occurrence X Detection

## Slide 15
FMEA Procedure (Cont.)
5. Calculate the Risk Priority Number (RPN)
6. Develop recommended actions, assign responsible persons, and take actions
  Give priority to high RPNs
  MUST look at highest severity
7. Assign the predicted Severity, Occurrence, and Detection levels and compare RPNs (before and after risk reduction)
15

## Slide 16
Rating Scales
Preferred Scales are1-10
Adjust Occurrence scales to reality figures for your company
16
Severity:
1 = Not Severe, 10 = Very Severe
Occurrence:
1 = Not Likely, 10 = Very Likely
Detection:
1 = Easy to Detect, 10 = Not easy to Detect

## Slide 17
The FMEA Form
17
Identify failure modes and their effects
Identify causes of the failure modes
and controls
Prioritize
Determine and assess actions

## Slide 18
Risk assessment with FMEA

## Slide 19
How capable are we of detecting the failure mode with our current controls?
Document current process controls!
Potential for occurrence!
Identify potential root causes of failure mode!
Determine Severity of failure mode!
Identify consequences of that failure!
Identify failure modes at each process step!
Risk Assessment with FMEA
Risk Priority Number (RPN).
Highest # equals Highest Risk!
Severity x Occurrence x Detectability = RPN
Use Like Pareto Chart to identify what items to address first.

## Slide 20
Risk Assessment with FMEA
Severity
Occurrence
Detection

## Slide 21
CASTING ATTACH TORQUE
OVER TORQUE
UNDER TORQUE
CROSS THREAD
CASTING FRACTURE
CASTING SEPARATION
CASTING SEPARATION
10
9
9
TORQUE WRENCH NOT CONTROLLED
TORQUE WRENCH NOT USED/ CONTROLLED
NO LEAD IN ON BOLT THREAD
4
DC TORQUE WRENCH USED / LINKED TO OMS
3
120
ADD TORQUE ALARM AND CALIBRATION AT START UP.
JENNY TONE
10
2
20
1
Risk Assessment with FMEA

## Slide 22
Risk Priority Number (RPN)
RPN is the product of the severity, occurrence, and detection scores
22
Severity
Occurrence
Detection
RPN
X
X
=

## Slide 23
FMEA, 10 Steps Checklist
23
10 Steps to Conduct a PFMEA
Review the process—Use a process flowchart to identify each process component
Brainstorm potential failure modes—Review existing documentation and data for clues
List potential effects of failure—There may be more than one for each failure
Assign Severity rankings—Based on the severity of the consequences of failure
Assign Occurrence rankings—Based on how frequently the cause of the failure is likely to occur
Assign Detection rankings—Based on the chances the failure will be detected prior to the customer finding it
Calculate the RPN—Severity X Occurrence X Detection
Develop the action plan—Define who will do what by when
Take action—Implement the improvements identified by your PFMEA team
Calculate the resulting RPN—Re-evaluate each of the potential failures once improvements have been made and determine the impact of the improvements